## Slide 1: AASHTOWare Project Estimator Presentation
Introduction
Obtaining an Estimator Account
Log in
What’s new in Version 2.13a-1
Estimator set up
Opening a catalog
Creating an estimate
Submittal into ProjectWise

## Slide 2: Definition of Estimator
Estimator is an interactive, PC-based, stand-alone cost estimation system for highway construction.
Part of AASHTO Trns•port Suite
Many U.S. states use Estimator including:
  NY, Maine, Maryland, Ohio, Pennsylvania, Vermont, Virginia, and District of Columbia

## Slide 4: What’s New in Estimator 2.13a-1
Global option “Catalog” tab added
Global option “Verifications” tab added
Global option “Numeric rounding” - Default now set to wT Precon settings
Agency users can now open estimates submitted by non-agency users without “wild card” user
Spreadsheet imports now include estimate- level, item-level and extra data options

## Slide 5: Obtain an Estimator® Account
Purchase Estimator® from InfoTech
  http://www.infotechfl.com/products/estimator.php
  Note: Link on CTDOT website
  Annual fee - $499 for each license
  Separate license is required for each State
  Please note new version 2.13a-1
Information about other AASHTO TRNS*PORT products can be found at:
  http://www.cloverleaf.net/

## Slide 6: Estimator® Log In
Obtain User Id/Password
  Consult Firm’s Estimator Administrator
Click on the Estimator Icon
  Consult Firm’s Estimator Administrator if no icon on desktop
Log in with the credentials that were supplied to you

## Slide 7: CTDOT Estimator Webpage
Estimator User Guide
Templates
New Item request Form
E-Mail Address for Questions/Information/User Id-Password
Navigation:
  http://www.ct.gov/dot/site/default.asp
  Navigate to “Doing Business with CONNDOT”
  Go to CTDOT AASHTO Trns*port Environment listed under the Engineering Resources
  Select Estimator

## Slide 9: Estimator User Guide Contents

## Slide 10: CTDOT Catalog Download
The latest Metric and English catalogs and item lists are available online at:
  http://www.ct.gov/dot/site/default.asp
  Navigate to “Doing Business with CONNDOT”
  Go to CTDOT AASHTO Trns*port Environment listed under the Engineering Resources
  Select Estimator
    The Estimator Catalogs (English and Metric) are listed
    Estimator User Guides are here also

## Slide 11: Global Options – General Tab Configure according to “CTDOT User’s Guide – Appendix B”
On the main menu, select Tools->Global Options

## Slide 12: Global Options – Numeric/Rounding

## Slide 13: Global Options – URLs

## Slide 14: Global Options – Tree Labels

## Slide 15: Global Options – Catalog

## Slide 16: Global Options – Verifications

## Slide 17: Open a Catalog
Catalog Tools>Open A Catalog or Switch Current Catalog
Select one of the following:
English 3 Year (ENG3YR)
Metric 5 Year (MET5YR)
English 5 Year (ENG5YR_REF_ONLY)
- Reference catalog for individual items only
- Do not use for entire estimates
Can open more than 1 catalog at a time – not recommended
Updates to the catalogs will be posted by AEC, on or about the first Wednesday of the month, on the Estimator webpage (sign up for e-alert notifications – Section B.1.3)

## Slide 18: Catalog Items
Requesting New Items – fill out request and submit through CTDOT consultant liaison
  Must be requested 6 weeks prior to the Final Design Plans (FDP) delivery date
Special Provisions
  Old “A” Items
  ** See Special Provisions **

## Slide 19: Creating An Estimate
Estimates are made up of an estimate header, a group list, and a group’s item list
Four ways to create:
  New Estimate: File>New
  Template: Download Templates
  Import Excel spreadsheet
  Copy an existing project
Save Often!

## Slide 20: Using Templates
Download template zip file from Estimator webpage
File>Import
Select template .xml file
Save
Add or delete items as necessary and update prices

## Slide 21: Templates
File>Import. Select template .xml file

## Slide 22: Creating an Excel Spreadsheet for Import
Item numbers must be formatted as
text with leading 0’s
“A” items numbers replaced with
** See Special Provisions **
in Supplemental Description column

## Slide 23: Sample Spreadsheet CTDOT Estimator Webpage

## Slide 24: Spreadsheet Tabs
Items Extra Data
Estimate Data
Note: Export of estimate must be done first

## Slide 25: File Import
Import Dialog Box
File>Import

## Slide 26: Estimate Import Spreadsheet Wizard Importing “Item-Level” Data

## Slide 27: Estimate Import Spreadsheet Wizard Importing “Estimate-Level” Data

## Slide 28: Estimate Import Spreadsheet Wizard Importing “Extra Data”

## Slide 29: Mapping Column Headings

## Slide 30: Project Header Information
Important – Information entered (or not entered) in this area may have a significant impact on total cost.
Fill out completely & accurately as possible!!

## Slide 31: Header Information
Estimate ID – Project number + “_CT”
Spec Year – 11 for English, 10 for metric
Automatically sets Base Date – must be reset to anticipated Letting date
  If Letting date not known, use FDP date + 70 days
Unit System – English or Metric
Latitude/longitude of Midpoint – Google Earth
  GPS latitude/longitude of midpoint fields are the decimal degree (DD:DDDD) equivalents of the latitude/longitude of midpoint fields. These fields fill in automatically.
Federal/State Project Number – Use Federal Aid Project (FAP) number if known; otherwise leave blank
Default Fund Package – Not being used (Leave blank)
Description – Same as project title

## Slide 32: Obtaining a Midpoint (Lat/Long) for Project
Open Google Earth
Type address in search box
Add a placemark

## Slide 33: Tools>Options 3D View Tab
Default setting

## Slide 34: Obtaining a Midpoint (Lat/Long) for Project continued
Center the placemark within the project limits.
  Note the latitude and longitude of the midpoint of the project – round to nearest minute

## Slide 35: Obtaining a Midpoint (Lat/Long) for Project continued
Enter the coordinates (lat/long) in the Estimator project header
The GPS lat/long of midpoint fields are the decimal degree (DD:DDDD) equivalents of the lat/long of the midpoint fields. These fields fill in automatically.

## Slide 36: Header Information

## Slide 37: Header Information Continued
Work Type – Selection based on the work of the “most costly” items
Highway type – Functional classification (from Highway Log)
Urban/Rural Type (from Highway Log)
Season – Season of the letting date (should coincide with base date)
  Fall (9/21 – 12/20)
  Spring (3/21 - 6/20)
  Summer (6/21 - 9/20)
  Winter (12/21 - 3/20)
County – Town, Statewide, District wide
District – (1, 1A, 2, 3, 3A, 4, HDQ)
Contingency – Estimate Total field uses a Contingency % in the calculation – list in notes section. Add inflation here also
Description –same as project title

## Slide 38: Header Information Continued
Estimated by – automatically filled with User ID
Checked by – Optional
Approved by – Optional
Estimate type – Scoping, 30%, 60%, 90%, Final, Addendum, change order, other
Notes page – list contingency/incidental percentages breakdowns/inflation; other notes
User ID

## Slide 39: Estimator Windows & Views
Estimator displays catalogs and estimates in windows
  Can open several estimates at a time
  Arrange windows (cascade or tile)
Tree
View
Grid View
Grid View

## Slide 40: Groups
Groups are based on funding source or Non-Contract Items
  Description must be added
  Non contract items will have 8888 in description
To add a group, select “Add Group” from the Edit menu
Group Descriptions

## Slide 41
To expand on a group, Click on GO

## Slide 42: Group Header
List the items for each group. Click on the yellow up arrow to go back to all groups.

## Slide 43: Items
Adding Items
  From Tree View
  From Grid View
  From All Items
  Using Go Button
  Drag and Drop from Catalog
(Tree view)
Right click and select “Add Item”
(Grid view)
Type in item number

## Slide 44: Items Continued
Find Item Button

## Slide 45: ITEM Properties
Item Properties
  Line Number
    Code used by other Trns*port software
  Item Number
  Supplemental Description
    Old “A” items
  Description
  Unit
  Quantity

## Slide 46: ITEMS Properties Con’t
  Unit price – cost of one unit of item
    Determined by the estimator or calculated from a cost sheet, bid history or reference price
  Extension – Unit price X Quantity
  Alt Code – if item is part of an alternate item list
  Price Source
    None – no active price basis
    Multiple – more than one type of active price basis
    Cost Sheet – based on equipment, labor and materials
    Reference Price – based on quotes or percentage
    Bid-based Price – based on historical bids
    Price Basis list
    Ad Hoc – entered by user

## Slide 47: Special Provisions
Former Special Provision item designation was “A”
  Current notation for Special Provision items is “** See Special Provisions **”
  Added in the Supplemental Description
  “Extra Data” must be entered by administrator

## Slide 48: Reference Prices and Percentages
Check Exclude Item From Reference Price Calculations
Add Reference Price
Add Reference Price ID name, Check Percentage and enter % amount

## Slide 50: Items Continued
All Items Tab
Go Button
All Items
Highlight
Estimate

## Slide 51: Sorting Items
Highlight Estimate in Tree View and select All Items tab
Sort by selecting any column heading
This example was sorted by Extension

## Slide 52: Alternate Items
Alternate items – bidder bids on one alternate
Can have alternate items or alternate groups

## Slide 53: More on Pricing
Bid Based Prices – Estimator puts updated bid histories of items at users fingertips.
Ad hoc
Updating prices

## Slide 54: Estimator Pricing
Bid History Regression

## Slide 55: Estimator Pricing
Bid History Average

## Slide 56: Estimator Pricing
Quantity out of range

## Slide 57: Estimator Pricing
No History Available

## Slide 58: Updating Prices
Pricing Updates are done when:
  Catalogs are updated
  Estimate imported from Excel spreadsheet or template
Can be done at
  Estimate Level
  Group Level
  Item Level
Must be initiated by the user - not automatic

## Slide 59: Updating Prices Continued
Highlight Estimate, Group or Item
Select Edit> Update Price Information
Detailed description in User’s Guide

## Slide 60: Final Estimate Submittal at FDP
Fill out checklist
Log into ProjectWise
Follow the steps outlined in Section 6.8 of Trns•port Estimator Procedures Guide

## Slide 62: Contact Information
Email at: DOT.TrnsPortEstimator@ct.gov
Ron Tellier
  Ronald.Tellier@ct.gov
  (860) 594-3285
Kathy Zimmerman
  Kathleen.Zimmerman@ct.gov
  (860) 594-3326
Julie Annino
  Julie.Annino@ct.gov
  (860) 594-2730