## Slide 1: Transit Score Presentation with Connecticut DOT Friday, September 9, 2011
1

## Slide 2: Agenda
2
Introduction & Overview of Transit Score
  Thomas Marchwinski, Sr. Director, Forecasting & Research NJ TRANSIT
Background of Transit Score and Use in Planning, Smart Growth
  Tom Marchwinski NJT
Possible Role in CDOT and for Smart Growth
  Discussion
Comments/Questions and Going Forward

## Slide 3
Transit Score:
A Screening Tool for Evaluating Community & Regional Suitability for Transit Investments
Background, Development and Use of Transit Score
Details of Transit Score for Planning
Use for Smart Growth
New Jersey Transit:
Thomas W. Marchwinski
Sr. Dir. of Forecasting and Research
3

## Slide 4
Transit Score- Background
Help inform the selection of appropriate transit investments and services for a given community
Screening tool to test and relate land use plans to transit service and investment at both a municipal and regional level
A function of the densities of population, employment and carless households
4

## Slide 5
Need for Transit Score
Local elected officials and real estate developers pressing for new transit lines
$$ are scarce – projects must be prioritized
Transit ridership is directly proportional to urban density, but many developers and local officials are not aware of that linkage
5

## Slide 6
Need for Transit Score
Need to simply and graphically show how the consequences of land-use planning and zoning decisions impact the prospects for success of proposed new transit lines and transit services.
Show impact of land use plans on potential for regular route bus service and access to transit stations (shuttles)
6
Notes: Land use

## Slide 7
Transit Score Update Project History
DVRPC ‘Transit Potential’ (1989, 1992) and NJ Transit Transit Score (2000).
NJT used in 2000 to evaluate its 2020 plan and fixed guideway extensions
Score factors were based on analyst judgment and accepted principles.
2005 to 2008 a project was undertaken to test, modernize, and technically strengthen the tool for use by more stakeholders.
7

## Slide 8
Calibrating the New Transit Score Model
A regression tested the relationship between various inputs and transit (bus/rail) JTW mode share (avg. origin and destination mode share by tract), as a proxy for Transit Score.
Impacts were tested for the DVRPC region, State of NJ, and combined area of the two (2,934 Census Tracts [2000]).
8
Notes: Jtw mode share proxy

## Slide 9
Calibrating the New Transit Score Model
A variety of inputs were initially tested (all densities gross):
  Population, worker, & housing unit density;
  Job density;
  0-car & 1-car household density;
  Median JTW travel time by origin & dest.;
  Presence of rail station within ½ mile; and
  Bus stop density.
9

## Slide 10
Calibrating the New Transit Score Model
Pop., worker, and housing unit densities were highly correlated, so pop. density was the only input tested in the calibration
Job density and 1-car household density were found to be not significant or significant and negative, and so the regression was re-run without these inputs
10

## Slide 11
Resulting “Full” Transit Score Equation
Transit Score =
[0.13*(Pop. per acre)] + [1.21*(Zero car HH per acre)] + [0.36*(Med. travel time for JTW trips originating in each area)] + [0.34*(Med. travel time for JTW trips terminating in each area)] +
[2.47 If rail station is located within one- half mile] + [14.99*(Bus stops per acre)]
-11.58 [constant]
Adjusted R^2 = 0.682
11

## Slide 12
Calibrating the Final Transit Score Model
The “full” Transit Score equation is interesting academically, but with limited practical use
The final Transit Score Model was calibrated using a subset of the original independent variables:
  Population density, Job density, and 0-Car household density
12

## Slide 13
Final Transit Score Model
Regression for the Transit Score Model was run with the constant suppressed, for simplicity of the final tool for end users
TRANSIT SCORE =
    0.41*(Population per land acre) +
    0.09*(Jobs per land acre) +
    0.74*(Zero car households per land acre)
13

## Slide 14
Setting the Transit Score Class Intervals
Raw numerical scores were grouped into categories based on:
  The distribution of scores
  The existing multimodal transit network
  NJ State Plan’s Planning Area designations
Score categories are associated with transit investments, which are indicated as appropriate, conditionally appropriate, or not appropriate
14

## Slide 15
DVRPC and New Jersey Score Map
15

## Slide 16
DVRPC Applications of Transit Score
Regional:
DVRPC Long Range Plan
Regional transit planning/analysis studies
Local:
Corridor studies
County / municipal / local planning
16

## Slide 17
REGIONAL: Score Changes 2000-2030
17

## Slide 18
LOCAL: NJ 322 – Sprawl Scenario
18

## Slide 19
LOCAL: NJ 322 – Smart Growth Scenario
19

## Slide 20
New Jersey Transit & Transit Score Project
NJ Transit is a multi-modal statewide transit agency serving multiple metropolitan areas. Primary use of Transit Score is for integrating good transit planning principals with local land use control
Transit Score Project was undertaken to assist NJ Office of Smart Growth in using Transit Score to assist municipalities in understanding relationship between land use polices and potential for transit services
20

## Slide 21: Classification of Transit Score into Categories based on Land Use & Transit Service Patterns
Categories relate to range of transit modes and services
“High Transit Potential” areas have highest densities and/or high amount of transit dependents
Potential by mode relates to Transit Score for both ends of a trip
Five Categories from “Low to “High” indicate broad potential for transit using New Jersey standards
21

## Slide 22: What Does Transit Score Mean for Statewide Planning?
Transit Score provides screening guide to indicate appropriate service level or type of transit in most areas
Map combined with specific criteria indicates potential for transit
Transit Score of Medium or Above is closely related to where existing transit service is located and approximates NJ State Plan growth areas
22

## Slide 23
Transit & Land Use Interaction
Transit Score can be used to track effectiveness of NJ State Plan in terms of key data (population, jobs) meeting different transit criteria
Provides ready tool for local officials to initially test viability of different land use patterns for range of transit services.
Screening of feasibility for different transit options to a few options for more detailed study in a timely manner. Focus on realistic alternatives.
23

## Slide 24
Transit Score Criteria Guidelines
Provide for minimum conditions to indicate which modes and services warrant further Study
Criteria were set to reflect NJ TRANSIT financial or service standards & experience from mid-2000’s
Provides range of fixed guideway, local transit services and intermodal guidelines with specific criteria
24

## Slide 25: Types of Transit Investment covered by Transit Score
Fixed Guideway Transit- Light Rail, Commuter Rail, Ferries, Bus Priority Treatment
Bus and Other Transit Services- New Services, Expanded Span & Frequency of Bus Service, Vanpools
Intermodal/Access to Transit-New Park & Ride, Shuttles, Terminals
25

## Slide 26: Applications of Transit Score Index in New Jersey
Used to Show Land Use/Transit Relationships & Screen Modal Options for a Central Jersey Transportation Study in Princeton Area. Interactive Testing of Land Use Changes Required to Support LRT in Several Corridors. Resulted in Elimination of several LRT Options. and eventual Route 1 BRT project
Joint Toll Bridge Commission used Transit Score to identify potential for transit service in its Crossings Study
Mercer County used for Master Plan process, as did Monmouth County for Rt. 79 corridor study. Pinelands Commission used for locating potential housing
DVRPC/NJTPA both use for various studies and feasibility work
26

## Slide 27
New Jersey Applications of Transit Score
State DOT is still (early 2011) considering using Transit Score as a screening criteria to allow traffic reduction credit for Highway Access Permits of new development in proximity to transit.
Would allow residential, non-retail employment in certain transit score areas to receive a reduction in auto trip generation for new projects. This reduces the impact for developers in transit friendly areas
27

## Slide 28: Use of Transit Score for Developer Credit for DOT Access Permit

## Slide 29: Transit Score Guide Book
Why the Guidebook
Available at CDOT
29

## Slide 30: Calculating Transit Score
Three Factors
Population Density
Employment Density
Zero-Car Household Density
Equation
Transit Score =
  [0.41*(Population per acre)]
  + [0.09*(Jobs per acre)]
  + [0.74*(Zero-car households per acre)]
30

## Slide 31: Transit Score Intervals-NJ
Category | Ranges
High | > 7.5
Medium-High | 2.5 to 7.5
Medium | 1.0 to 2.4
Marginal | 0.6 to 0.9
Low | < 0.6
31

## Slide 32: CT Ranges could be Different
Category | Ranges
High | TBD
Medium-High | TBD
Medium | TBD
Marginal | TBD
Low | TBD
32

## Slide 33: Distribution of Scores for New Jersey (2000)
33
Category | Population | Employment | Households | Land Area
High | 23.4% | 16.9% | 22.8% | 1.5%
Medium-High | 31.0% | 29.4% | 31.6% | 6.9%
Medium | 23.8% | 29.3% | 23.7% | 12.5%
Marginal | 6.5% | 9.5% | 6.8% | 7.0%
Low | 15.3% | 14.9% | 15.1% | 72.1%
Total | 8,414,000 | 3,962,000 | 3,310,000 | 7,418 Sq. Mi.

## Slide 34: Detailed Investment Criteria & Conditions (High)
34
TRANSIT SCORE CATEGORY (Score) | FIXED GUIDEWAY TRANSIT FEASIBILITY CONDITIONS | BUS & OTHER TRANSIT SERVICE CRITERIA | INTERMODAL/ ACCESS TO TRANSIT
HIGH (>7.5) | Rapid Transit-Only if direct connection to Manhattan or Philadelphia or 150,000+ jobs in center Commuter Rail as a Destination or Terminal- Only if a with 60,000+ jobs in municipality High Capital Cost Electric LRT- 33% of line can be in tunnel or elevated. Must have 30,000+ jobs in center, 60,000 jobs preferred. Medium/Low Capital Cost Electric LRT- Must have 30,000+ jobs in center or municipality to be terminal for line. Bus Priority Treatment-On major arterials with 40+ buses/peak hr. direction Bus Only Ramps/Lanes- On limited access roads/connectors to Regional Centers with 60,000+ jobs Ferry Services to High Score areas with 60,000+ jobs. Fixed Guideway or Local Transit connecting service. | Express Bus Service to areas as a Destination or Terminal if 60,000+ jobs in center or municipality. High Intensity Local Bus Service. All day service span (16-24 hours) with average 20 minute frequency over the span of a day. Express Mini-Bus service from High Score areas to suburban employment centers with 30,000+ jobs. Vanpools and vanpool subsidies which do not compete with existing transit. | Major Multi-Modal Terminals Limited Park-Ride Facilities in Structured Parking Bus/Rail Transfer Centers and Feeder Bus services

## Slide 35
35
Detailed Investment Criteria & Conditions (Medium)
TRANSIT SCORE CATEGORY (Score) | FIXED GUIDEWAY TRANSIT FEASIBILITY CONDITIONS | BUS & OTHER TRANSIT SERVICE CRITERIA | INTERMODAL/ ACCESS TO TRANSIT
MEDIUM (1.0 to 2.4) | Commuter Rail/Diesel LRT to High Transit Score areas with 60,000+ jobs in center or municipality, usually with existing Rail ROW or service extension Medium/Low Cost LRT- Only if area is surrounded by Medium-High Score areas. Bus Priority- Same as Medium-High except limited to Primary Arterials such as State Highways with LOS "D" or worse in Peak Hour. Recreational Transit- Rail/Express Bus/Ferry to seasonal tourist areas as a destination. Must have minimum 30% of housing units in seasonal units and 1500 seasonal units in a municipality. Ferry with Park-Ride access to High Transit Score Areas with 60,000+ jobs | Minimum Intensity Local Bus Service- Span of 8-12 Hours/Day, with average frequency of 30-60 minutes over day. Local Circulator Bus Service in Rural Centers in State Plan. (PA 3, 4, & 5) Span of 8-12 Hours/Day with average frequency of 30-60 minutes Mini-Bus service to Suburban Employment Centers from line-haul transit service. Preferred minimum of 10,000 jobs in employment center. Express "Reverse" Mini-Bus service from High Score areas to Suburban Employment Centers with 30,000+ jobs. | Shuttle Bus Walk Access to Rail/LRT /Express Bus if minimum of 500 boarding riders at stop and Gross Housing Density of 2+ units per acre. Remote Parking and Shuttle Bus to Rail/LRT/Express Bus if housing density not met. Surface Park-Ride Only for Express Bus/ Commuter Rail/ Ferry except in constrained areas with 1000+ peak period riders

## Slide 36
36
2005 Transit Score Map (Existing)

## Slide 37: 2035 Transit Score Map (Trend)
37

## Slide 38: Transit Options
38

## Slide 39
Smart Growth is…
Expanded choices
39

## Slide 40
State House
Smart Growth Is Redevelopment
40

## Slide 41: Transit Oriented Developments
What is TOD
What it can be
Why they are connected to Transit Score
How they are different than Transit Score
41

## Slide 42: TOD is really Center-based Development
True benefit is coordinated land use that builds more sustainable communities. A tenet of the NJ State Plan
What is its potential?
    Positive influence on community health
    Creates opportunity for strong, stable ratable base
    Reduces household transportation costs
    Can influence societal interaction
    Positive influence on environment (reduced VMT, re-use and redevelopment, support conservation inititaives, etc)
    Leverages resources
Transit Score a tool to “scenario plan”
Transit Score = Density Calcs / TOD = Design Character
42
Notes: empasis

## Slide 43: High Transit Score Places
43
Copyright 2010 NJ Transit
Dover
Cranford
Camden

## Slide 44: High Transit Score Places
44
Copyright 2010 NJ Transit
Hoboken
New Brunswick
Newark

## Slide 45: Others…Medium High Transit
45
Copyright 2010 NJ Transit
Rutherford
Gladstone
Rutherford
Madison
Secaucus
Morristown Dev.
45

## Slide 46: Others…
46
Copyright 2010 NJ Transit
South Orange

## Slide 47: LRT
Camden
Copyright 2010 NJ Transit
47

## Slide 48: BUS / BRT
DSC
GO Bus
GO Bus
Copyright 2010 NJ Transit
48

## Slide 49: BUS / BRT
Port Imperial
Helix
Copyright 2010 NJ Transit
49

## Slide 50: Regional Context for a Transit Score
50

## Slide 51: Potential Use of Transit Score
Master Plan Updates
Visioning
MPO Studies
Corridor Studies
Smart Growth Analysis
51

## Slide 52: Transit/Land Use Interaction & System Measurement
Can modify demographic forecasts or land use development to illustrate viability of possible transit services
Would be used as a tool to assist municipalities in understanding relationship between future development and potential for transit service
Statewide categories can track effectiveness of moving State to more transit friendly environment in terms of amount of population, jobs at different levels of Transit Score
52
Notes: Last bullet emphasis

## Slide 53: Role of Transit Score in Land Use Planning
) TESTING POTENTIAL OF ALTERNATIVE LAND USE OPTIONS
Change density and location of development- results in new Transit Scores and identifies potential viability of alternative transit options & services
Quick ability to identify amount of land use change needed to support different transit modes in any type of study area
53

## Slide 54: Role of Transit Score in Land Use & Transit Planning
“Screening” of Possible Feasibility for Transit Down to a Few Options for More Detailed Analysis & Study by Agency
  Reduces Time Spent on Impractical Options, Focus on Realistic Alternatives
  Answers Question “Did you Look at this Option?” Without Time & Expense of Full Feasibility Analysis
Defensible Methods for Screening with Public
Link Land Use with appropriate transit service/investment
54

## Slide 55: Transit Score Role in Land Use Planning
Sketch Planning for Transit Potential
Specific Transit Score Criteria by mode/service is used to Relate typical transit Ridership Volumes, Services & Comparable Ridership data with land use data
By Combining Estimated Transit Scores & Specific Criteria by mode or service in study area, an “Order-of-Magnitude” Transit Potential can be estimated for alternative land use patterns or demographics, especially for municipal circulation plans and plan endorsement
Does not mean NJT will have funding to implement transit services, but does identify potential
55

## Slide 56: Conclusions
Transit score methodology can be used by towns to identify a range of transit services and modes that could be supported by land use patterns in a given geographic area.
It narrows the range of transit options to the most realistic based on NJ Transit experience
Can quickly test alternative land use scenarios & inform process of land use planning on a REGIONAL or MUNICIPAL level with decision makers regarding transit.
Can be used to advocate for more detailed transit studies
Transit Score Guidebook can be used to inform and guide this type of planning
56
Notes: quick

## Slide 57: Conclusions
Transit Score can be Customized to Local Conditions Using Local Data.
Can be Applied to any Geographic Area
Most Data is Readily Available (Census)
Easy to Use & Explain. Gross Densities Used in Most Cases for Simplicity
For Quick Response Analysis, can be integrated with other Regional & NJ Transit data.
Saves Time & Money by Limiting Detailed Examination of Transit to a Few Options
57

## Slide 58: Connecticut Specific Issues
Connections to Larger Region (NY/Boston) similar to New Jersey
Medium Sized cities with focused local bus transit networks and some rail service (New Haven, Hartford, Stamford)
Need for reverse commute and transit in suburban areas to link job centers
Access Methods to Existing Commuter Rail (New Haven Line, branches)

## Slide 59: Connecticut Specific Issues
Where does new or improved transit play a role in connection with Smart Growth?
How can Transit Score help with analysis of alternatives of both transit and land use?
Development of Connecticut Specific Transit Score Categories (Based on transit experience in CT. and local examples)
Access to Transit Options (Parking, shuttles ) and local transit services

## Slide 60: Adapting Transit Scores for CT (draft)
60

## Slide 61: Questions & Comments
61